## Slide 1: Continuity Testers
Supplies - Per Tester
1 Tin
1 Buzzer
1 LED
1 long black wire (stranded,10-12”)
1 long red wire (stranded,10-12”)
1 9-Volt Battery (cheep at BatteriesAndButter.com)
1 9-Volt Battery clip
Supplies – To Share
Electrical Tape
Wire Strippers
Nail & Hammer (or Drill)
Optional: Toothpick, Needle-Nose Plyers

## Slide 2: Continuity Testers: 1. Do the Following in Any Order
Strip Wires
Find:
  1 buzzer
  1 black wire
  1 red wire
  1 battery clip
  1 wire stripper
Strip ~ ½ inch off each end of each wire
Hammer Holes
Find:
  1 tin
  1 nail
  1 hammer
Hammer 3 holes into tin (keep holes within 3 inches of each other)
Use nail to widen one hole (to put LED through)
Misc. Prep
Cut 6 ~1-inch pieces of electrical tape to use later
Put 1 piece of tape on buzzer (to make quieter)
With help of toothpick or needle-nose plyers, bend tips of 1 LED (any color)up to make “hooks”
Attach battery clip to battery
Do NOT test LED - You could fry it!

## Slide 3: 2. Connect Red battery wire to red buzzer wire
Buzzers have polarity – only work in 1 direction
Touch black ends together to ensure buzzer works
Tape connection to insulate and hold in place

## Slide 4: 2. Connect black battery wire to Short (negative) LED leg
Touch black buzzer wire to long (positive) end of LED to ensure LED works. If not, reverse LED connections
Tape connection to insulate and hold in place

## Slide 5: 3. Connect Long Black wire to Long (positive) end of LED
Touch black buzzer wire to long black wire to ensure circuit works.
Tape connection to insulate and hold in place

## Slide 6: 4. Connect Long red wire to Black Buzzer Wire
Touch long red wire to long black wire to ensure circuit works.
Tape connection to insulate and hold in place

## Slide 7: 5. Loosely tie knot near taped end of red and black wires
This will protect the circuit should a wire get tugged

## Slide 8: 6. Package circuit into tin
Put light of LED through the largest hole & tape in place.
Thread the long red and black wires through the other two holes.
Put the battery and buzzer anywhere inside.
Test to ensure no “shorts”. Add extra insulation if needed.
Close tin. Wrap with tape if desired.

## Slide 9: Uses for continuity tester
Teaching circuits
Testing circuits/conductivity
Reusable quiz sheets/game boards
Steady hand games (e.g. “Operation”)