## Slide 1: Safe-Stop Robots
Supplies - Per Robot
Yogurt cup (or plastic cup)
2 x1.5” copper tape
3” Red wire
4” Black wire
5” Black wire
1.5V motor (try AllElectronics.com)
1/3 Hot glue stick
AA Battery (try BatteriesAndButter.com)
1” Foam Tape
2” Foam Tape
Supplies – To Share
Masking tape
Wire strippers/cutters
Scissors
Ruler (if supplies aren’t pre-cut)

## Slide 2
1. Cut wires & strip ¼ - ½ inch from each end
Save 2 of the stripped rubber stubs!
3” Red wire
4” Black wire
5” Black wire
2. Poke motor shaft through glue stick segment, off center

## Slide 3
4. Attach copper tape to both sides of cup using rubber nubs to raise copper above rim
Keep ~1” along outside, to tape wires to later
(Cut-Away View)

## Slide 4
3. Put Red wire through right tab, and 5” Black wire through left Tab
Keeping colors consistent makes it easier to troubleshoot students’ projects.

## Slide 5
5. Use foam tape to attach battery and motor to cup in a T shape
Use ~1” for motor
Use ~2” for battery
Put positive side to right
Ensure glue tick has clearance
(Bird’s Eye View – Cup Upside-down)

## Slide 6
6. Tape Attach red wire to positive side of battery, and short (4”) black wire to negative side
(Bird’s Eye View – Cup Upside-down)

## Slide 7
7. Tape short black wire to copper tape on left, and tape long black wire to copper tape on right
We tape the wire to the non-adhesive side of the copper tape because it conduct electricity better.
(Bird’s Eye View – Cup Upside-down)

## Slide 8: 8: Create board for Robot
Use foam board, poster board, or two pieces of card stock taped together.
Tape aluminum foil on
Optional: Make split between two sides, and have students explain why the robot won’t move, even if both sides are touching metal.